## Slide 1: Irrigation System Using LoRa
Myungwoo Yang, Subeen Jeong, Jeongjun Lee
Chungnam National University, Purdue University

## Slide 2: Introduction
What is problem?
  Drought
    There is a severe drought in the western United States.
  Water usage rate
    Most automatic irrigation systems use more water than is necessary.

## Slide 3: Introduction
Important of method
  Low Power
    Most of the time, the farm is difficult to provide electronic power,
    our system have to require low power.
  Water usage rate
    As the farm grows bigger, Reducing water usage has great economic benefits.

## Slide 4: Introduction
Our method
  LoRa
    low-power wide-area network technology
  MAD auto-irrigation algorithm
    Algorithms to reduce water usage

## Slide 5: Introduction
  LoRa
    LoRa (Long Range) is a low-power wide-area network (LPWAN) technology

## Slide 6: Introduction
  Auto irrigation system – with LoRa
Data Sensing
Humidity, soil moisture, temperature
End Node
(LoRa Shield & Bee)
LoRa Gateway
Internet
Server
Connect between
LoRa and Internet
Save Data
Action
irrigation
Control Action

## Slide 7: Introduction
  MAD auto-irrigation algorithm
  Management allowable depletion(MAD) specifies the maximum amount of soil water the irrigation manager chooses to allow the crop to extract from the active rooting zone between irrigations.
  Only a portion of the available water holding capacity is easily used by the crop before crop water stress develops.

## Slide 8: Introduction
  MAD auto-irrigation algorithm

## Slide 9: Introduction
  MAD auto-irrigation algorithm
AWS
MAD
Irrigation
Condition
Input
Output
AWS : Amount of Water Stored in the active zone of soil

## Slide 10: Introduction
  MAD auto-irrigation algorithm
  Irrigation Set Time
  Normal Onions Rooting Depth (ft): 1
  MAD(%) for onions: 30
  Net Irrigation = () x MAD
  Application Efficiency of Drip or Micro Spinkler (%) = 80~ 90%
  Gross Application(GA) = Net Application / Application Efficiency
Notes: Net Irrigation : 흙이 물을 얼마나 흡수 할 수 있는지
Application Efficiency of Drip : 흙을 뿌렸을 때 흙이 얼마나 물을 흡수 하는지 나타낸다. 스프링쿨러마다 달라진다.

## Slide 11: Introduction
  MAD auto-irrigation algorithm
  Irrigation Set Time
[pic.1~2] How to calculate

## Slide 12: Introduction
  MAD auto-irrigation algorithm
  Irrigation Set Time
    Where GA= Gross Application
    A = Area, square feet
    Q = Flow Rate per plant, gallons per hour
    T = (GA x A) / 1.6 x Q
    T is an irrigation set time.

## Slide 13: Summary
  We built an irrigation system with low power and long distance communication.
  We built an irrigation system that uses less water then previous irrigation system.

## Slide 14: Conclusion
Future Work:
  Use Weather API
    We will use weather api for prediction of rains. This is helpful for reducing water usage
  Collect Data
    We want to grow crops and collect data. This data will be used our paper and tell us how good our system is.

## Slide 15: Thank you